Section Sixteen

###### Lower Ouachita Smackover

Priority Watershed

2011-2016 NPS Pollution Management Plan

ADEQ Planning Segment 2D ( HUC 08040201

Introduction

Segment 2D occupies the south central part of Arkansas and covers two 8-digit hydrologic unit code (HUC) watersheds, Lower Ouachita Smackover (08040201) and Lower Ouachita-Bayou De Loutre (08040202). The Lower Ouachita Smackover watershed covers Bradley, Dallas, Ouachita, Cleveland, Columbia, Nevada, and Union counties. Segment 2D encompasses the lower Ouachita River and its tributaries from the confluence of the Little Missouri and Ouachita Rivers to the Louisiana state line. The major tributaries are Moro Creek, Camp Creek, Champagnolle Creek, and Smackover Creek. Figure 16.1 shows a map of the watershed.

Figure 16.1: Map of Lower Ouachita Smackover watershed

http://www.arkansaswater.org/NPSmanagementPlan/Images/Chapter16/Figure16.1_Lower_Ouachita_Smackover_Watershed_Map.jpg

Source: GeoStor

Assessment

The summary of water quality condition is described from the most current 305(b) report from the Arkansas Department of Environmental Quality (ADEQ) and other sources as cited appropriately. The following was stated in 2008 305(b) report (IWQMAR, 2008):

“The waters within this segment have been designated as suitable for fish propagation, wildlife, primary and secondary contact recreation, as well as public, industrial, and agricultural water supplies. Monitored data were used as the basis of assessing 220.2 miles of stream. An additional 125.4 miles were evaluated bringing the total number of miles assessed within this segment to 345.6 stream miles.

The Lower Ouachita River, Champagnolle, and Moro Creeks have fish consumption advisories due to mercury contamination. A consumption advisory has been placed on 66.3 miles of the Ouachita River, 20.0 miles of Champagnolle Creek, and 12 miles of Moro Creek.

Some of the most severe water quality problems exist in the unnamed tributary from El

Dorado Chemical Company (ELCC), in Flat Creek and Salt Creek. The ELCC tributary contains toxic ammonia levels, very high nitrates, high minerals (SO4/ TDS), and metals

(Copper and zinc); the source is from the El Dorado Chemical Company discharge. Flat

Creek and Salt Creek have very high minerals (CL/ SO4/TDS) and metals (Copper and zinc).

The exact source is unknown, but these drainage basins are from the northern edge of El Dorado where numerous oil and brine processing and storage facilities exist along with numerous abandoned pumping facilities. These streams enter Smackover Creek below the ambient monitoring station. TMDLs were completed in October 2002, and in October 2003. Additional point source controls are also needed to address these issues.”

The University of Arkansas Department of Biological and Agricultural Engineering has used the Soil and Water Assessment Tool (SWAT) to model selected priority watersheds for the 2011-2016 Nonpoint Source (NPS) Pollution Management Plan under contract with the Arkansas Natural Resource Commission (ANRC). Appendix B describes SWAT modeling process and the data used to estimate sediment and nutrient concentration for 12-digit HUC sub-watersheds.

Brief Description of Land Uses in the Watershed

# Figure 16.2 shows land use in the Lower Ouachita Smackover watershed in 2006.

# Figure 16.2: Distribution of Lower Ouachita Smackover watershed land uses, 2006

# http://www.arkansaswater.org/NPSmanagementPlan/Images/Chapter16/Figure16.2_Land_Use_Map.jpg

# Source: Center for Advanced Spatial Technologies (CAST), 2006 LULC coverage

# The following provides a partial snapshot of the watershed:

- Nearly 6 percent of the watershed’s land area is under pasture and 76 percent of the watershed is under forest (CAST, 2006. The remaining land usage includes construction, waterbodies, etc.

- Approximately 39,809 people live in the watershed (BAEG, 2011). Throughout the watershed, population has been decreasing between 2000 and 2010, with the exception of Cleveland county. Most decrease took place in Dallas County (-11.9 percent) whereas the least decrease was in Columbia county (-4.1 percent)(UALR, 2011).

#### Water Quality/Program Goals

The Lower Ouachita Smackover watershed has been designated as a priority for the first time by ANRC for the 2011-2016 NPS Pollution Management Plan .

Based on the most current List of Impaired Waterbodies published by the Arkansas Department of Environmental Quality (ADEQ), the impaired segments of the Lower Ouachita Smackover watershed can be viewed at the following links:

http://arkansaswater.org//index.php?option=com_content&task=view&id=14&Itemid=30

http://www.adeq.state.ar.us/water/branch_planning/pdfs/303d_list_2008.pdf.

The long-term goal of the priority watershed program is to reduce pollutants to levels that will restore all designated uses. The short-term goal of the program is to measurably reduce pollutants of concern that reach waters of the Lower Ouachita Smackover watershed, targeting sub-watersheds where implementation can have the greatest impact. These goals will be achieved through implementation of a Nine Element Plan.

# Objectives and Milestones

Based on SWAT and other available analysis, ANRC will review available data and select sub-watersheds for targeting of implementation funds. Data that may be considered in targeting includes, but is not limited to, the modeled loads for sediment and phosphorus, percentage of intact woody riparian vegetation, density of unpaved roads, number of stream road crossings, rural population density, intensity of row crop agriculture, degree of urbanization, and potential sources of pollutants. Other factors may also be considered at the discretion of ANRC, including but not limited to, local institutional capacity, input from the NPS Pollution Management Plan Stakeholder Group, local watershed groups or other agencies, availability of funds, and other factors.

The 2011-2016 NPS Pollution Management Plan includes statewide programs aimed at reducing pollutant loads from land uses that have the potential to impact water quality. These land uses and programs to reduce their water quality impacts are described in more detail in earlier sections of the 2011-2016 NPS Pollution Management Plan.

The following objectives and milestones were identified with input from the NPS Pollution Management Plan stakeholders. Table 3.1 identifies cooperating entities that will partner to implement the NPS program in the Lower Ouachita Smackover watershed. Cooperating entities are described in an earlier section of this plan.

14.1 Continue development of the Nine Element Plan until the U.S. Environmental Protection Agency (EPA) approval is obtained.

Timeline for Milestones: October 2011 – September 2016

14.2. Continue to develop support for implementation of the Nine Element Plan among potential cooperating entities and the general public.

Timeline for Milestones: October 2011 – September 2016

14.3. Provide technical and financial assistance to local cooperating entities to implement the Nine Element Plan as resources allow.

Timeline for Milestones: October 2011 – September 2016

14.4. As resources allow, use remote sensing and Geographical Information Systems (GIS) analysis to identify sub-watersheds where more extensive assessment is needed. Conduct targeted geomorphological and bio-assessment to identify and target implementation of streambank stabilization projects for high impact sites (e.g., a geomorphologic study of logjams and assess beaver populations to determine their impact on streambank erosion and other studies).

Timeline for Milestones: October 2011 – September 2016

14.5. Continue to develop models to represent sediment and nutrient loads in the watershed and in-stream processes to enable prioritization of implementation projects in sub-watersheds.

Timeline for Milestones: October 2011 – September 2016

14.6. Continue to focus on best management practices (BMP) implementation to improve conservation practices for erosion control, sediment retention, irrigation management and nutrient management on row crop and animal agriculture and forestland. As appropriate, direct technical assistance to landowners in targeted watersheds giving emphasis to developing new conservation plans and areas that connect established riparian corridors.

Timeline for Milestones: October 2011 – September 2016

14.7. Continue to provide and improve extensive education and training to promote BMP implementation (e.g., risk management, demonstrations to acquaint landowners and municipalities with the conservation practices most effective in reducing runoff, sediment detachment and transport, including but not limited to no-till, conservation till, ridge till, pipe drop outlets, riparian zone management, and wetland restoration).

Timeline for Milestones: October 2011 – September 2016

14.8. Continue to encourage landowners to establish riparian buffer strips, grass drainage ways, stabilize streambanks, and restore riparian areas

Timeline for Milestones: October 2011 – September 2016

14.9. Continue to secure conservation easements through donations as the opportunity arises in an effort to protect lands along Arkansas River and its tributaries from development that would result in further NPS pollution.

Timeline for Milestones: October 2011 – September 2016

14.10. Continue to increase public awareness and provide education to build support for citizen action to improve water quality in the watershed.

Timeline for Milestones: October 2011 – September 2016

14.11. Build constituency for improved water quality by increasing volunteerism and promoting recreational use of the river (e.g., recruiting volunteers for cleanups, streambank restoration and other activities utilizing the Arkansas Stream Team program and other conservation groups as well as increasing public recreational access to the river with trails and boat ramps).

Timeline for Milestones: October 2011 – September 2016

14.12. Encourage county and municipal elected officials as well as contractors, homebuilders, and consulting engineers to participate in construction and urban education programs to improve stormwater management.

Timeline for Milestones: October 2011 – September 2016

14.13. Coordinate conservation planning within a watershed area to take full advantage of cost-share programs for riparian habitat improvement such as the Wetland Reserve Program (WRP), the Conservation Reserve Program (CRP), the Wetland and Riparian Zone Tax Credit Program (through ANRC), and other programs.

Timeline for Milestones: October 2011 – September 2016

14.14. Encourage plans for alternative irrigation water supply and supplemental stream augmentation, including off-stream storage of surplus flows.

Timeline for Milestones: October 2011 – September 2016

14.15. Continue aquatic life assessments to assess response of waterbodies to NPS control measures as resources allow.

Timeline for Milestones: October 2011 – September 2016

14.16. Continue to provide public education on proper application, storage and disposal of pesticides, regulations, and potential hazards of misuse (e.g., encourage use of FARM*A*SYST and HOME*A*SYST programs to assess potential pollution hazards).

Timeline for Milestones: October 2011 – September 2016

14.17. Continue to provide education to rural homeowners and builders on proper construction and maintenance of onsite waste disposal systems.

Timeline for Milestones: October 2011 – September 2016

14.18. Continue to provide technical assistance and make available financial assistance to agricultural operations where cost-share is a component of approved 319(h) implementation projects.

Timeline for Milestones: October 2011 – September 2016

#### Timeline for Milestones

Provided sufficient financial and human resources are available to the cooperating state and local agencies and nonprofit organizations working together in the Lower Ouachita Smackover watershed, the short-term objectives of this plan can be met within five years of program initiation. Fully implementing management measures within the watershed to restore all designated uses is a longer term endeavor. A goal of this plan is to fully meet designated uses within 15 years.

Program Coordination

There is currently no single entity in the Lower Ouachita Smackover watershed with the authority to implement the Nine Element Plan. ANRC will work with cooperating entities in the watershed to promote voluntary coordination and incorporate conditions requiring cooperation in grant agreements, as appropriate.

Federal Consistency

The lead agency for each statewide program is responsible for working with federal partners to promote federal consistency. Statewide programs and their lead agencies are identified in the cooperating entities section of the 2011-2016 NPS Pollution Management Plan.

#### Program Tracking and Monitoring

Water quality monitoring data will be used to evaluate the effectiveness of NPS Pollution Management activities in the Lower Ouachita Smackover watershed. ADEQ is responsible for maintaining the state’s water quality inventory. Figure 16.3 shows monitoring stations in the watershed.

Figure 16.3: Monitoring stations in the Lower Ouachita Smackover watershed

http://www.arkansaswater.org/NPSmanagementPlan/Images/Chapter16/Figure16.3_Monitoring_Stations_Map.jpg

Source: GeoStor

The NPS Pollution Management Plan may include as a condition of funding pre- and post-project measurements of changes in water quality. The NPS Pollution Management Plan encourages cooperating entities working in the watershed to meet annually to report on their activities of the previous year and discuss their successes, failures and future needs of their programs. The local watershed group is a logical convener for these discussions. Local cooperators are encouraged to compile this information, along with a summary of available water data and land use trends, into an annual watershed status report published and distributed in the watershed and to interested parties outside the watershed.

References Cited

# BAEG, 2011. County-wise Population Data. Biological and Agricultural Engineering Department. University of Arkansas Division of Agriculture: Little Rock, AR.

# CAST, 2006. Land Use-Land Cover Data. Biological and Agricultural Engineering Department. University of Arkansas: Fayetteville, AR.

Integrated Water Quality Monitoring and Assessment Report (IWQMAR). 2008. Arkansas Department of Environmental Quality: Little Rock, AR. Available at http://www.arkansaswater.org//Documents/305b/2008_305b.pdf.

# UALR, 2011. Percent Change in Total Population. Available at http://argis.ualr.edu/2010Census/Change_in_Pop_2000_to_2010_by_County.pdf.